## Slide 1
Project Presentation
CHITKARA UNIVERSITY
Diesel Filter Modernization:
Predictive Maintenance and Intelligent
Fault Diagnosis Using Machine Learning
and Data Analytics
Nabh Jindal
Roll No: [Your Roll Number]
Department of Computer Sciences
Mentor: [Mentor Name]

## Slide 2
CHITKARA UNIVERSITY
Introduction
Nabh Jindal | Dept. of Computer Sciences
2 / 17
Introduction
The Problem
DPFs capture >99% of PM2.5 but degrade nonlinearly. Fixed-interval maintenance misses variable soot/ash loading.
Current Gap
Calendar/mileage-based protocols create bimodal failure: unnecessary replacements on easy routes, missed failures on harsh ones.
The Opportunity
Low-cost OBD-II sensors + fleet telematics + mature ML frameworks enable data-driven predictive maintenance.
Emission Standards
Euro VI, BS-VI, EPA Tier 4 Final place DPF at center of fleet compliance. Proper maintenance = regulatory compliance.

## Slide 3
CHITKARA UNIVERSITY
Research Objectives
Nabh Jindal | Dept. of Computer Sciences
3 / 17
Research Objectives
1
Can ML models predict DPF clogging with sufficient accuracy and lead time for proactive maintenance?
2
Which ML architecture best captures temporal dynamics of soot accumulation and filter degradation?
3
What are quantifiable improvements in maintenance efficiency vs. fixed-interval protocols?
4
How can a practical, edge-deployable filter health monitoring system be architected?

## Slide 4
CHITKARA UNIVERSITY
Literature Review
Nabh Jindal | Dept. of Computer Sciences
4 / 17
Literature Review
Author(s) | Contribution | Key Finding
Bisset (1984) | First analytical DPF regeneration model | Wall-flow monolith thermal regeneration
Konstandopoulos & Johnson | Pressure drop model for wall-flow filters | Foundation of production DPF monitoring
Theissler et al. | Random Forest for ECU fault classification | 8-12% improvement over rule-based systems
Zhao et al. | LSTM for vibration-based wear prediction | Recurrent models excel at long-term degradation
Gao et al. | Bayesian NN for DPF state estimation | 89.7% accuracy with uncertainty quantification
Wang et al. | XGBoost for fuel contamination detection | 93.1% accuracy on 4-class fuel fault task
Author(s)
Contribution
Key Finding

## Slide 5
CHITKARA UNIVERSITY
Dataset & Data Collection
Nabh Jindal | Dept. of Computer Sciences
5 / 17
Dataset & Data Collection
42
Vehicles
3 fleet operators
2.8M
Observations
1 Hz sampling
18
Months
Jan 2023 – Jun 2024
3
Regions
Punjab, Haryana, Rajasthan
Vehicle Types:
18 Light Commercial Trucks (3.5–12t GVW)
16 Heavy-Duty Haulage Vehicles (>25t GVW)
8 Agricultural Tractors (75–130 hp)
Ground Truth:
DPF: Dashboard warnings + workshop inspection + gravimetric weighing
Fuel Filter: Laboratory analysis + spectrometric fuel analysis

## Slide 6
CHITKARA UNIVERSITY
Feature Engineering
Nabh Jindal | Dept. of Computer Sciences
6 / 17
Feature Engineering
Feature | Description | Role
Differential Pressure (ΔP) | Pressure drop across DPF (kPa) | Primary soot loading indicator
Exhaust Temp Diff (ΔT) | Upstream - downstream EGT (°C) | Regeneration activity indicator
Engine Load RoC | Derivative of normalized torque | Duty cycle severity metric
Fuel Consumption Rate | Instantaneous fuel flow (L/hr) | Operating intensity
Soot Accumulation Index | Model-derived soot mass (g/L) | Composite health metric
Coolant Temperature | Engine thermal state (°C) | Warm-up / overheating proxy
Vehicle Speed | Instantaneous speed (km/hr) | Duty cycle classification
Regeneration Flag | Binary active regen indicator | Cycle status
Feature
Description
Role
Top features by mutual information + RFE: ΔP, ΔT, SAI, Engine Load RoC

## Slide 7
CHITKARA UNIVERSITY
ML Models
Nabh Jindal | Dept. of Computer Sciences
7 / 17
Machine Learning Models
Random Forest
300 trees, depth 20, min leaf 5
Interpretable baseline + feature importance
XGBoost
500 estimators, lr 0.05, depth 6
Best for structured tabular classification
SVM (RBF)
C=10, γ=0.01
Classical maximum-margin baseline
LSTM
2-layer, 128 units, dropout 0.3
Long-range temporal dependencies
CNN-LSTM
64 conv filters + 128 LSTM units
Dual-timescale: local transients + cumulative

## Slide 8
CHITKARA UNIVERSITY
Experimental Setup
Nabh Jindal | Dept. of Computer Sciences
8 / 17
Experimental Setup
Data Split & Validation
Vehicle-stratified 80/20 split
34 vehicles train / 8 vehicles test
10% validation for early stopping
Vehicle-level stratification ensures generalization to unseen operational contexts
LSTM/CNN-LSTM: 60-min rolling windows, 10-min stride
Training Configuration
Optimizer: Adam (lr = 1e-3)
LR reduction on plateau (factor 0.5, patience 5)
Early stopping: patience 15 epochs
Features normalized to [0,1] using train-set stats only
5-fold CV for hyperparameter selection

## Slide 9
CHITKARA UNIVERSITY
Results: DPF Clog Prediction
Nabh Jindal | Dept. of Computer Sciences
9 / 17
Results: DPF Clog Prediction
# | Model | Accuracy | F1-Score | Recall | AUC-ROC
1 | CNN-LSTM | 94.3% | 0.937 | 0.941 | 0.978
2 | LSTM | 91.7% | 0.912 | 0.918 | 0.961
3 | XGBoost | 88.4% | 0.879 | 0.875 | 0.944
4 | Random Forest | 85.1% | 0.847 | 0.843 | 0.928
5 | SVM | 79.6% | 0.791 | 0.784 | 0.876
#
Model
Accuracy
F1-Score
Recall
AUC-ROC
Chart: 
| CNN-LSTM | LSTM | XGBoost | Random Forest | SVM
Accuracy % | 94.3 | 91.7 | 88.4 | 85.1 | 79.6

## Slide 10
CHITKARA UNIVERSITY
Results: Fuel Filter Classification
Nabh Jindal | Dept. of Computer Sciences
10 / 17
Results: Fuel Filter Fault Classification
# | Model | Accuracy | F1 (macro) | Recall | AUC-ROC
1 | XGBoost | 91.8% | 0.914 | 0.907 | 0.967
2 | CNN-LSTM | 89.5% | 0.891 | 0.886 | 0.958
3 | Random Forest | 86.3% | 0.859 | 0.855 | 0.941
4 | LSTM | 83.7% | 0.832 | 0.826 | 0.921
5 | SVM | 76.4% | 0.758 | 0.752 | 0.889
#
Model
Accuracy
F1 (macro)
Recall
AUC-ROC
Chart: 
| Normal Aging | Microbial | Water Ingress | Wax Crystal. | Bypass Fail | Seal Fail
Per-Class Accuracy % | 92.1 | 89.3 | 97.2 | 96.8 | 84.1 | 88.7

## Slide 11
CHITKARA UNIVERSITY
Discussion
Nabh Jindal | Dept. of Computer Sciences
11 / 17
Key Insight: Architecture-Task Fit
CNN-LSTM wins DPF (94.3%)
DPF clog prediction is a trajectory forecasting problem with dual-timescale dynamics:
CNN layer extracts local transient patterns (hard acceleration, regen events)
LSTM integrates them into a cumulative degradation trajectory
This maps directly onto the known physics of DPF soot loading.
XGBoost wins Fuel Filter (91.8%)
Fuel filter fault classification is a static pattern recognition problem:
Each fault produces a characteristic signature at any moment, independent of preceding trajectory
Gradient-boosted trees excel at hierarchical feature interaction rules for tabular data
Temporal models add noise, not signal, for this task.

## Slide 12
CHITKARA UNIVERSITY
Maintenance Impact
Nabh Jindal | Dept. of Computer Sciences
12 / 17
Maintenance Scheduling Impact
-34.2%
Unnecessary
Replacements
3.1 → 2.0 per vehicle-year
-61.4%
Unplanned
Downtime
DPF overloading & bypass
47 hrs
Mean Warning
Window
σ = 8.2 hours
Chart: 
| Replacements/yr | Downtime Events
Fixed Interval | 3.1 | 5.7
ML-PdM | 2 | 2.2

## Slide 13
CHITKARA UNIVERSITY
System Architecture
Nabh Jindal | Dept. of Computer Sciences
13 / 17
Edge-Cloud System Architecture
Edge Inference
Node
ARM Cortex-M7
INT8 quantized
1-min intervals
Telemetry
Aggregation
Batch upload
Sensor logs
Fleet gateway
Cloud Analytics
Engine
Model training
Retraining
Fleet analytics
Maintenance
Decision
Alert tiers
θ=0.35 / θ=0.15
Scheduling
Model Update
Pipeline
OTA updates
Incremental
Edge deploy
Edge: INT8-quantized XGBoost (fuel filter) + pruned LSTM (DPF) | 256 KB RAM | <0.8% accuracy loss | Outputs: DPF health (0-1), fault class probabilities (6-class), regen recommendation

## Slide 14
CHITKARA UNIVERSITY
Fuel Filter Fault Taxonomy
Nabh Jindal | Dept. of Computer Sciences
14 / 17
6-Class Fuel Filter Fault Taxonomy
Normal Aging
Gradual sediment accumulation over service life
92.1%
Microbial Contamination
Biofouling with characteristic flow oscillations
89.3%
Water Ingress
Free water accumulation with distinctive temp-pressure signature
97.2%
Wax Crystallization
Low-temperature paraffin wax formation in fuel
96.8%
Filter Bypass
Collapsed media causing unfiltered flow (hardest to detect)
84.1%
Housing Seal Failure
Seal degradation producing unfiltered bypass flow
88.7%

## Slide 15
CHITKARA UNIVERSITY
Limitations
Nabh Jindal | Dept. of Computer Sciences
15 / 17
Limitations
Geographic Scope
Dataset restricted to northern India. Climate, road conditions, fuel sulfur content may differ from European/North American/SE Asian fleets.
Study Duration
18 months may not capture full seasonal variation in wax crystallization or long-term ash accumulation dynamics.
SAI Reliability
Soot Accumulation Index is a model-derived estimate, not direct gravimetric measurement. Systematic error varies with filter aging and fuel quality.
Data Privacy
Continuous collection of vehicle location, speed, load data raises privacy concerns. Requires clear data minimization policies.

## Slide 16
CHITKARA UNIVERSITY
Future Work
Nabh Jindal | Dept. of Computer Sciences
16 / 17
Future Research Directions
Digital Twin Integration
Couple ML model with physics-based simulation of DPF/DOC/SCR for physically interpretable predictions including ash capacity estimates.
Federated Fleet Learning
Train shared global models by aggregating gradient updates across fleet operators without centralizing raw data.
Multi-Sensor Fusion
Integrate acoustic emission sensors for early detection of substrate cracking and ash delamination not visible in pressure-temperature data.
Transfer Learning
Domain adaptation and fine-tuning pre-trained feature extractors to accelerate deployment on new engine families.

## Slide 17
CHITKARA UNIVERSITY
Thank You
Nabh Jindal
jindalnabh2004@gmail.com
Department of Computer Sciences