## Slide 1
Project Presentation (22CS421)
On
Diesel Filter Modernization:
Predictive Maintenance and Intelligent Fault Diagnosis
Using Machine Learning and Data Analytics
Nabh Jindal
Roll No: 221090592
Department of Computer Sciences
Mentor: Dr. Gifty Gupta
Chitkara University, Punjab

## Slide 2
Introduction
2
The Problem: DPFs capture >99% of PM2.5 but degrade nonlinearly. Fixed-interval maintenance misses variable soot/ash loading.
Current Gap: Calendar/mileage-based protocols create bimodal failure: unnecessary replacements on easy routes, missed failures on harsh ones.
The Opportunity: Low-cost OBD-II sensors + fleet telematics + mature ML frameworks enable data-driven predictive maintenance.
Emission Standards: Euro VI, BS-VI, EPA Tier 4 Final place DPF at center of fleet compliance. Proper maintenance = regulatory compliance.

## Slide 3
Research Objectives
3
Can ML models predict DPF clogging with sufficient accuracy and lead time for proactive maintenance?
Which ML architecture best captures temporal dynamics of soot accumulation and filter degradation?
What are quantifiable improvements in maintenance efficiency vs. fixed-interval protocols?
How can a practical, edge-deployable filter health monitoring system be architected?

## Slide 4
Literature Review
4
Bisset (1984): First analytical DPF regeneration model — wall-flow monolith thermal regeneration.
Konstandopoulos & Johnson: Pressure drop model for wall-flow filters — foundation of production DPF monitoring.
Theissler et al.: Random Forest for ECU fault classification — 8-12% improvement over rule-based systems.
Zhao et al.: LSTM for vibration-based wear prediction — recurrent models excel at long-term degradation.
Gao et al.: Bayesian NN for DPF state estimation — 89.7% accuracy with uncertainty quantification.
Wang et al.: XGBoost for fuel contamination detection — 93.1% accuracy on 4-class fuel fault task.

## Slide 5
Dataset & Data Collection
5
42 Vehicles across 3 fleet operators | 2.8M Observations at 1 Hz sampling | 18 Months (Jan 2023 - Jun 2024) | 3 Regions: Punjab, Haryana, Rajasthan
Vehicle Types: 18 Light Commercial Trucks (3.5-12t GVW), 16 Heavy-Duty Haulage Vehicles (>25t GVW), 8 Agricultural Tractors (75-130 hp)
Ground Truth — DPF: Dashboard warnings + workshop inspection + gravimetric weighing
Ground Truth — Fuel Filter: Laboratory analysis + spectrometric fuel analysis

## Slide 6
Feature Engineering
6
Differential Pressure (ΔP): Pressure drop across DPF (kPa) — Primary soot loading indicator
Exhaust Temp Diff (ΔT): Upstream - downstream EGT (°C) — Regeneration activity indicator
Engine Load RoC: Derivative of normalized torque — Duty cycle severity metric
Fuel Consumption Rate: Instantaneous fuel flow (L/hr) — Operating intensity
Soot Accumulation Index: Model-derived soot mass (g/L) — Composite health metric
Vehicle Speed: Instantaneous speed (km/hr) — Duty cycle classification
Regeneration Flag: Binary active regen indicator — Cycle status
Top features by mutual information + RFE: ΔP, ΔT, SAI, Engine Load RoC

## Slide 7
Machine Learning Models
7
Random Forest: 300 trees, depth 20, min leaf 5 — Interpretable baseline + feature importance
XGBoost: 500 estimators, lr 0.05, depth 6 — Best for structured tabular classification
SVM (RBF): C=10, γ=0.01 — Classical maximum-margin baseline
LSTM: 2-layer, 128 units, dropout 0.3 — Long-range temporal dependencies
CNN-LSTM: 64 conv filters + 128 LSTM units — Dual-timescale: local transients + cumulative degradation

## Slide 8
Experimental Setup
8
Data Split: Vehicle-stratified 80/20 split — 34 vehicles train / 8 vehicles test; 10% validation for early stopping
Validation: Vehicle-level stratification ensures generalization to unseen operational contexts; LSTM/CNN-LSTM: 60-min rolling windows, 10-min stride
Optimizer: Adam (lr = 1e-3) with LR reduction on plateau (factor 0.5, patience 5)
Early Stopping: Patience 15 epochs; Features normalized to [0,1] using train-set stats only
Hyperparameter Selection: 5-fold cross-validation

## Slide 9
Results: DPF Clog Prediction
9
1. CNN-LSTM: Accuracy 94.3% | F1-Score 0.937 | Recall 0.941 | AUC-ROC 0.978
2. LSTM: Accuracy 91.7% | F1-Score 0.912 | Recall 0.918 | AUC-ROC 0.961
3. XGBoost: Accuracy 88.4% | F1-Score 0.879 | Recall 0.875 | AUC-ROC 0.944
4. Random Forest: Accuracy 85.1% | F1-Score 0.847 | Recall 0.843 | AUC-ROC 0.928
5. SVM: Accuracy 79.6% | F1-Score 0.791 | Recall 0.784 | AUC-ROC 0.876

## Slide 10
Results: Fuel Filter Fault Classification
10
1. XGBoost: Accuracy 91.8% | F1 (macro) 0.914 | Recall 0.907 | AUC-ROC 0.967
2. CNN-LSTM: Accuracy 89.5% | F1 (macro) 0.891 | Recall 0.886 | AUC-ROC 0.958
3. Random Forest: Accuracy 86.3% | F1 (macro) 0.859 | Recall 0.855 | AUC-ROC 0.941
4. LSTM: Accuracy 83.7% | F1 (macro) 0.832 | Recall 0.826 | AUC-ROC 0.921
5. SVM: Accuracy 76.4% | F1 (macro) 0.758 | Recall 0.752 | AUC-ROC 0.889

## Slide 11
Discussion: Architecture-Task Fit
11
CNN-LSTM wins DPF (94.3%): DPF clog prediction is a trajectory forecasting problem with dual-timescale dynamics. CNN layer extracts local transient patterns; LSTM integrates them into a cumulative degradation trajectory, mapping directly onto the known physics of DPF soot loading.
XGBoost wins Fuel Filter (91.8%): Fuel filter fault classification is a static pattern recognition problem. Each fault produces a characteristic signature at any moment, independent of preceding trajectory. Gradient-boosted trees excel at hierarchical feature interaction rules for tabular data.

## Slide 12
Maintenance Scheduling Impact
12
-34.2% Unnecessary Replacements: From 3.1 to 2.0 per vehicle-year
-61.4% Unplanned Downtime: Eliminating DPF overloading and bypass events
47 hrs Mean Warning Window: σ = 8.2 hours — providing substantial lead time for proactive action

## Slide 13
Edge-Cloud System Architecture
13
Edge Inference Node: ARM Cortex-M7, INT8 quantized, 1-min intervals
Telemetry Aggregation: Batch upload, sensor logs, fleet gateway
Cloud Analytics Engine: Model training, retraining, fleet analytics
Maintenance Decision: Alert tiers θ=0.35 / θ=0.15, scheduling
Model Update Pipeline: OTA updates, incremental, edge deploy
Edge specs: INT8-quantized XGBoost (fuel filter) + pruned LSTM (DPF) | 256 KB RAM | <0.8% accuracy loss | Outputs: DPF health (0-1), fault class probabilities (6-class), regen recommendation

## Slide 14
6-Class Fuel Filter Fault Taxonomy
14
Normal Aging (92.1%): Gradual sediment accumulation over service life
Microbial Contamination (89.3%): Biofouling with characteristic flow oscillations
Water Ingress (97.2%): Free water accumulation with distinctive temp-pressure signature
Wax Crystallization (96.8%): Low-temperature paraffin wax formation in fuel
Filter Bypass (84.1%): Collapsed media causing unfiltered flow (hardest to detect)
Housing Seal Failure (88.7%): Seal degradation producing unfiltered bypass flow

## Slide 15
Limitations
15
Geographic Scope: Dataset restricted to northern India. Climate, road conditions, fuel sulfur content may differ from European/North American/SE Asian fleets.
Study Duration: 18 months may not capture full seasonal variation in wax crystallization or long-term ash accumulation dynamics.
SAI Reliability: Soot Accumulation Index is a model-derived estimate, not direct gravimetric measurement. Systematic error varies with filter aging and fuel quality.
Data Privacy: Continuous collection of vehicle location, speed, load data raises privacy concerns. Requires clear data minimization policies.

## Slide 16
Future Research Directions
16
Digital Twin Integration: Couple ML model with physics-based simulation of DPF/DOC/SCR for physically interpretable predictions including ash capacity estimates.
Federated Fleet Learning: Train shared global models by aggregating gradient updates across fleet operators without centralizing raw data.
Multi-Sensor Fusion: Integrate acoustic emission sensors for early detection of substrate cracking and ash delamination not visible in pressure-temperature data.
Transfer Learning: Domain adaptation and fine-tuning pre-trained feature extractors to accelerate deployment on new engine families.

## Slide 17
Thank You
Nabh Jindal
jindalnabh2004@gmail.com | Department of Computer Sciences